VHDL

Entity
Name plate of the design: specify input and output ports as well as what kind of ports they are.

Architecture
How the circuit is going to behave/function. Multiple architectures can map to the same entity. Can only contain concurrent statements (everything executes at the same time).
1. Data flow: use concurrent signal assignment statements
ex: c <= a and b;
2. Behavioral: high level descriptions, consists of a set of assignment statements to represent behavior.
ex: if a = ‘1’ and b = ‘1’ then c <= ‘1’ else c <= ‘0’ end if;
3. Structural: components from libraries connected together, each component can be individually simulated.
ex: using two Half_Adder entities to create one Full_Adder architecture.

Inside architecture we use signals which are essentially wires, usually std_logic typed. You connect components with signals.

Assignment
<= to connect wires
:= to assign variables

Modes (driver direction)
IN
Value can be read but not assigned by entity
OUT
Value can be assigned but not read by entity
INOUT
Value can be read or assigned by entity
BUFFER

Data Types
BIT: supports values 0 and 1
BOOLEAN: true or false
std_logic: defined in std_logic_1164
- U: uninitialized (only simulated)
- X: unknown (only simulated)
- 0
- 1
- Z: high impedance
  - Logic 0 means you are sinking current
  - Logic 1 means you are sourcing current
  - Z: neither sourcing nor sinking current
- W: unknown
- L: low logic 0
  - Something near 0V
- H low logic 1
  - Something near 5V or other high
- -: don’t care